## Slide 1: FIL SPM Course May 2011 Spatial preprocessing
Ged Ridgway
With thanks to John Ashburner
and the FIL Methods Group

## Slide 2: fMRI time-series movie
Notes: Auditory example data

## Slide 3: Preprocessing overview
REALIGN
COREG
SEGMENT
NORM WRITE
SMOOTH
ANALYSIS

## Slide 4: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 5: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Unified segmentation
Gaussian smoothing

## Slide 6: Representation of imaging data
Three dimensional images are made up of voxels
Voxel intensities are stored on disk as lists of numbers
The image “headers” contain information on
  The image dimensions
    Allowing conversion from list -> 3D array
  The “voxel-world mapping”
    matrix subscripts -> world/physical/mm coordinates
Can rigidly reorient images by changing their (affine) voxel-world mapping

## Slide 7: Types of registration in SPM
Manual reorientation
Rigid intra-modal realignment
  Motion correction of fMRI time-series
Rigid inter-modal coregistration
  Aligning structural and (mean) functional images
Affine inter-subject registration
  First stage of non-linear spatial normalisation
  Approximate alignment of tissue probability maps

## Slide 8: Types of registration in SPM – Nonlinear
Spatial normalisation using basis functions
  Registering different subjects to a standard template
Unified segmentation and normalisation
  Warping standard-space tissue probability maps to a particular subject (can normalise using the inverse)
DARTEL / Geodesic Shooting
  High-dimensional large-deformation warps from smooth flows
  Normalisation to group’s average shape template

## Slide 9: Manual reorientation
Image “headers” contain information that lets us map from voxel indices to “world” coordinates in mm
Modifying this mapping lets us reorient (and realign or coregister) the image(s)

## Slide 10: Manual reorientation

## Slide 11: Manual reorientation – Reslicing
Reoriented (1x1x3 mm voxel size)
Resliced
(to 2 mm cubic)

## Slide 12: Reslicing / Interpolation
Applying the transformation parameters, and re-sampling the data onto the same grid of voxels as the target image
  AKA reslicing, interpolation, regridding, transformation, and writing (as in normalise - write)
Nearest neighbour gives the new voxel the value of the closest corresponding voxel in the source
Linear interpolation uses information from all immediate neighbours (2 in 1D, 4 in 2D, 8 in 3D)
NN and linear interp. correspond to zeroth and first order B-spline interpolation, higher orders use more information in the hope of improving results

## Slide 13: Linear interpolation – 1D
f(x)
?
a
b
x
f(a)
f(b)
x
f

## Slide 14: Linear interpolation – 1D
0
1
x
f(0)
f(1)
f(x)
x0
x1

## Slide 15: Linear interpolation – 2D
Nearest neighbour
  Take the value of the closest voxel
Tri-linear
  Just a weighted average of the neighbouring voxels
  f5 = f1 x2 + f2 x1
  f6 = f3 x2 + f4 x1
  f7 = f5 y2 + f6 y1

## Slide 16: B-spline Interpolation
B-splines are piecewise polynomials
A continuous function is represented by a linear combination of basis functions
2D B-spline basis functions of degrees 0, 1, 2 and 3
Nearest neighbour and trilinear interpolation are the same as B-spline interpolation with degrees 0 and 1.

## Slide 17: Quantifying image alignment
Registration intuitively relies on the concept of aligning images to increase their similarity
  This needs to be mathematically formalised
  We need practical way(s) of measuring similarity
Using interpolation we can find the intensity at equivalent voxels
  (equivalent according to the current estimates of the transformation parameters)

## Slide 18: Voxel similarity measures
Mean-squared difference
Correlation coefficient
Joint histogram measures
Pairs of voxel intensities

## Slide 19: Automatic image registration
Quantifying the quality of the alignment with a measure of image similarity allows computational estimation of transformation parameters
This is the basis of both realignment and coregistration in SPM
  Allowing more complex geometric transformations or warps leads to more flexible spatial normalisation
Automating registration requires optimisation...

## Slide 20: Optimisation
Find the “best” parameters according to an “objective function” (minimised or maximised)
Objective functions can often be related to a probabilistic model (Bayes -> MAP -> ML -> LSQ)
Value of parameter
Objective function
Global optimum (most probable)
Local optimum
Local optimum

## Slide 21: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Unified segmentation
Gaussian smoothing

## Slide 22: Motion in fMRI
Can be a major problem
  Increase residual variance and reduce sensitivity
  Data may get completely lost with sudden movements
  Movements may be correlated with the task
  Try to minimise movement (don’t scan for too long!)
Motion correction using realignment
  Each volume rigidly registered to reference
  Least squares objective function
Realigned images must be resliced for analysis
  Not necessary if they will be normalised anyway

## Slide 23: Residual Errors from aligned fMRI
Slices are not acquired simultaneously
  rapid movements not accounted for by rigid body model
Image artefacts may not move according to a rigid body model
  image distortion, image dropout, Nyquist ghost
Gaps between slices can cause aliasing artefacts
Re-sampling can introduce interpolation errors
  especially tri-linear interpolation
Functions of the estimated motion parameters can be modelled as confounds in subsequent analyses

## Slide 24: fMRI movement by distortion interaction
Subject disrupts B0 field, rendering it inhomogeneous
  distortions occur along the phase-encoding direction
Subject moves during EPI time series
  Distortions vary with subject position
  shape varies (non-rigidly)

## Slide 25: Correcting for distortion changes using Unwarp
Estimate movement parameters.
Estimate new distortion fields for each image:
estimate rate of change of field with respect to the current estimate of movement parameters in pitch and roll.
Estimate reference from mean of all scans.
Unwarp time series.

+
Andersson et al, 2001

## Slide 26: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Unified segmentation
Gaussian smoothing

## Slide 27: Inter-modal coregistration
Match images from same subject but different modalities:
  anatomical localisation of single subject activations
  achieve more precise spatial normalisation of functional image using anatomical image.

## Slide 28: Inter-modal similarity measures
Seek to measure shared information in some sense
For example Mutual Information and related metrics
Statistical measure of information – entropy
Entropy is a property of a probability distribution
Probabilities can be estimated from histograms
Mutual information considers both images’ histograms and their joint histogram

## Slide 29: Joint and marginal histograms

## Slide 30: Joint histogram based registration
Joint histogram sharpness correlates with image alignment Mutual information and related measures attempt to quantify this
Initially registered T1 and T2 templates
After deliberate misregistration (10mm relative x-translation)

## Slide 32: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Unified segmentation
Gaussian smoothing

## Slide 33: Spatial Normalisation

## Slide 34: Spatial Normalisation - Reasons
Inter-subject averaging
  Increase sensitivity with more subjects
    Fixed-effects analysis
  Extrapolate findings to the population as a whole
    Mixed-effects analysis
Make results from different studies comparable by aligning them to standard space
  e.g. The T&T convention, using the MNI template

## Slide 35: Spatial Normalisation – Limitations
Seek to match functionally homologous regions, but...
  No exact match between structure and function
  Different cortices can have different folding patterns
  Challenging high-dimensional optimisation
    Many local optima
Compromise
  Correct relatively large-scale variability (sizes of structures)
  Smooth over finer-scale residual differences

## Slide 36: Standard spaces
The MNI template follows the convention of T&T, but doesn’t match the particular brain Recommended reading: http://imaging.mrc-cbu.cam.ac.uk/imaging/MniTalairach
The Talairach Atlas
The MNI/ICBM AVG152 Template
Notes: Also DICOM scanner-based voxel-world mapping

## Slide 37: Coordinate system sense
Analyze™ files are stored in a left-handed system
Talairach space has the opposite (right-handed) sense
Mapping between them requires a reflection or “flip”
  Affine transform with a negative determinant
x
y
z
x
y
z
z
x
y
Rotated example
Notes: On the left, the x-axis has been flipped. Note that we can’t rotate between the resulting coordinate systems, whereas we can between the right-hand one and the boxed one.

## Slide 38: Spatial Normalisation – Procedure
Starts with an affine transformation
  Fits overall shape and size, good initialisation
Refines registration with non-linear deformations/warps
Algorithm simultaneously minimises
  Mean-squared difference (intramodal, cf. Unified Seg.)
  Squared distance between parameters and their expected values (more on this soon…)
Requires appropriate template(s)

## Slide 39: Spatial Normalisation – Initial Affine
12 degree of freedom (DF)
  3 DF for translation
  3 DF for rotation
  3 DF for scaling or zooming
  3 DF for shearing or skewing

## Slide 40: Spatial Normalisation – Warping
Deformations are modelled with a linear combination of non-linear basis functions

## Slide 41: Spatial Normalisation – DCT basis
The lowest frequencies of a 3D discrete cosine transform (DCT) provide a smooth basis
plot(spm_dctmtx(50, 5))
spm_dctmtx(5,5)
ans =
0.447 0.602 0.512 0.372 0.195
0.447 0.372 -0.195 -0.602 -0.512
0.447 0.000 -0.633 -0.000 0.633
0.447 -0.372 -0.195 0.602 -0.512
0.447 -0.601 0.512 -0.372 0.195
% Note, pinv(x)=x’, projection P=x*x’ P{n} = x(:,1:n)*x(:,1:n)’
P{N} == eye(N)
P{n<N} projects to smoother approx.
Notes: Analytical derivatives available: d(cos(x)) = -sin(x)dx
Note, plot appears continuous because 50 samples Note, although discretised, still orthogonal

## Slide 42: Spatial Normalisation – Results
Non-linear registration
Affine registration

## Slide 43: Spatial Normalisation – Overfitting
Template
image
Affine registration.
(SSE = 472.1)
Non-linear
registration
without
regularisation.
(SSE = 287.3)
Non-linear
registration
using
regularisation.
(SSE = 302.7)
Without regularisation, the non-linear normalisation can introduce unnecessary deformation

## Slide 44: Spatial Normalisation – regularisation
The “best” parameters according to the objective function may not be realistic
In addition to similarity, regularisation terms or constraints are often needed to ensure a reasonable solution is found
  Also helps avoid poor local optima
  Can be considered as priors in a Bayesian framework, e.g. converting ML to MAP:
    log(posterior) = log(likelihood) + log(prior) + c

## Slide 45: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Unified segmentation
Gaussian smoothing

## Slide 46: Unified segmentation and normalisation
MRI imperfections make normalisation harder
  Noise, artefacts, partial volume effect
  Intensity inhomogeneity or “bias” field
  Differences between sequences
Normalising segmented tissue maps should be more robust and precise than using the original images ...
… Tissue segmentation benefits from spatially-aligned prior tissue probability maps (from other segmentations)
This circularity motivates simultaneous segmentation and normalisation in a unified model

## Slide 47: Summary of the unified model
SPM8 implements a generative model
  Principled Bayesian probabilistic formulation
Gaussian mixture model segmentation with deformable tissue probability maps (priors)
  The inverse of the transformation that aligns the TPMs can be used to normalise the original image
Bias correction is included within the model

## Slide 48: Mixture of Gaussians (MOG)
Classification is based on a Mixture of Gaussians model (MOG), which represents the intensity probability density by a number of Gaussian distributions.
Image Intensity
Frequency

## Slide 49: Modelling inhomogeneity
A multiplicative bias field is modelled as a linear combination of basis functions.
Corrupted image
Corrected image
Bias Field

## Slide 50: Tissue Probability Maps
Tissue probability maps (TPMs) are used as the prior, instead of the proportion of voxels in each class
ICBM Tissue Probabilistic Atlases. These tissue probability maps are kindly provided by the International Consortium for Brain Mapping, John C. Mazziotta and Arthur W. Toga.

## Slide 51: Deforming the Tissue Probability Maps
Tissue probability images are warped to match the subject
The inverse transform warps to the TPMs

## Slide 52
Tissue probability maps of GM and WM
Spatially normalised BrainWeb phantoms (T1, T2, PD)
Cocosco, Kollokian, Kwan & Evans. “BrainWeb: Online Interface to a 3D MRI Simulated Brain Database”. NeuroImage 5(4):S425 (1997)

## Slide 53: Contents
Registration basics
Motion and realignment
Inter-modal coregistration
Spatial normalisation
Unified segmentation
Gaussian smoothing

## Slide 54: Smoothing
Why would we deliberately blur the data?
  Improves spatial overlap by blurring over minor anatomical differences and registration errors
  Averaging neighbouring voxels suppresses noise
  Increases sensitivity to effects of similar scale to kernel (matched filter theorem)
  Makes data more normally distributed (central limit theorem)
  Reduces the effective number of multiple comparisons
How is it implemented?
  Convolution with a 3D Gaussian kernel, of specified full-width at half-maximum (FWHM) in mm
Notes: Spatial normalisation is never exact, so homologous regions can never be precisely registered. Furthermore, due to the noisy nature of the BOLD signal, activations from different scans can be slightly offset, thereby cancelling each other out. Smoothing spreads out the different areas and reduces the discrepancy.

## Slide 55
Example of
Gaussian smoothing in one-dimension
A 2D Gaussian Kernel
The Gaussian kernel is separable we can smooth 2D data with two 1D convolutions.
Generalisation to 3D is simple and efficient
Notes: (A convolution is a kind of very general moving average.) First you convolve in one direction, than in the other two directions.
A general rule of thumb is to use a smoothing kernel of 6 mm for single subject analyses and a smoothing kernel of 8 or 10 mm when you are going to do a group analysis.

## Slide 56: References
Friston et al. Spatial registration and normalisation of images. Human Brain Mapping 3:165-189 (1995).
Collignon et al. Automated multi-modality image registration based on information theory. IPMI’95 pp 263-274 (1995).
Ashburner et al. Incorporating prior knowledge into image registration. NeuroImage 6:344-352 (1997).
Ashburner & Friston. Nonlinear spatial normalisation using basis functions. Human Brain Mapping 7:254-266 (1999).
Thévenaz et al. Interpolation revisited. IEEE Trans. Med. Imaging 19:739-758 (2000).
Andersson et al. Modeling geometric deformations in EPI time series. Neuroimage 13:903-919 (2001).
Ashburner & Friston. Unified Segmentation. NeuroImage 26:839-851 (2005).
Ashburner. A Fast Diffeomorphic Image Registration Algorithm. NeuroImage 38:95-113 (2007).

## Slide 57: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 58: Preprocessing (fMRI only)
fMRI time-series
Motion corrected
Mean functional
REALIGN
SEGMENT
NORM WRITE
SMOOTH
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
MNI Space
TPMs

## Slide 59: Preprocessing overview
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
NORM WRITE
SMOOTH
TPMs
ANALYSIS
Input
Output
Segmentation
Transformation
(seg_sn.mat)
Kernel
(Headers changed)
MNI Space

## Slide 60: Preprocessing with Dartel
fMRI time-series
Motion corrected
Mean functional
REALIGN
COREG
Anatomical MRI
SEGMENT
DARTEL NORM 2 MNI & SMOOTH
TPMs
(Headers changed)
ANALYSIS
DARTEL CREATE TEMPLATE
...